Booting BBB from USB:
Steps:

1. Do the partitions of your USB stick as same as Sdcard partition, and copy the files to the /boot partitioin.
2. Copy the root file system to the FirstRootFs folder
3. Connect the USB stick to the board.
4. Now boot the board, and your board should have the u-boot to use the USB booting of your kernel and root file system.
5. Once your board booted and stop it in u-boot prompt.

U-boot# usb start
starting USB...
USB0: scanning bus 0 for devices... 1 USB Device(s) found
       scanning usb for storage devices... 1 Storage Device(s) found

U-boot# usb part 0
Partition Map for USB device 0 -- Partition Type: DOS

Part Start Sector Num Sectors UUID Type
  1 2048 237568 000935d2-01 0c Boot
  2 239616 15192064 000935d2-02 83

U-boot# ext2ls usb 0:2 /boot
<DIR> 4096 .
<DIR> 4096 ..
        3574064 vmlinuz-3.14.4.1-bone-armhf.com
<DIR> 4096 dtbs
<SYM> 31 zImage
        2556914 System.map-3.14.4.1-bone-armhf.com
        120500 config-3.14.4.1-bone-armhf.com

U-boot# ext2load usb 0:2 ${loadaddr} /boot/zImage
3574064 bytes read in 2624 ms (1.3 MiB/s)

U-boot# ext2load usb 0:2 ${fdtaddr} /boot/dtbs/am335x-boneblack.dtb
31547 bytes read in 486 ms (62.5 KiB/s)

U-Boot# setenv bootargs console=${console} root=/dev/sda2 rw rootdelay=5

U-Boot# bootz ${loadaddr} - ${fdtaddr}