U-boot Commands:

bdinfo	: print Board Info structure
 The bdinfo command (short: bdi) prints the information that U-	Boot passes about the board such as memory addresses and	sizes, clock frequencies, MAC address, etc. This information	is mainly needed to be passed to the Linux kernel.
conin	: print console devices and information
 The output contains the device name, flags, and the current usage.
base	: It shows base address ex: 0x00000000
bootd	: This command will boot the device default i.e run 'bootcmd'
bootm	: boot application image from memory
bootelf	: Boot from an elf image in memory. load ELF image at [address] via	program headers (-p) or via section headers (-s).
bootp	: Boot image via network using BOOTP/TFTP protocol
bootvx	: Boot vxWorks from an ELF image
bootz	: boot linux zImage image from memory
cmp	: memory compare
cp	: memory copy
crc32	: compute CRC32 checksum
dfu	: Device firmware upgrade. We can upgrade through tftp and usb controller
dhcp	: boot image via network using DHCP/TFTP protocol
dm	: Driver model low level access
echo	: echo args to console
editenv	: edit environment variable
eeprom	: EEPROM sub-system . Read/write eeprom
env	: environment handling commands
exit	: exit script
ext2load	: load binary file from a Ext2 filesystem on interface
ext2ls	: list files in a directory (default /)
ext4load	: load binary file from a Ext4 filesystem
ext4ls	: list files in a directory (default /)
ext4size	: determine a file's size
ext4write	: create a file in the root directory
false - do nothing, unsuccessfully
fastboot- use USB Fastboot protocol
fatinfo - print information about filesystem
fatload - load binary file from a dos filesystem
fatls - list files in a directory (default /)
fatsize - determine a file's size
fatwrite- write file into a dos filesystem
fdt - flattened device tree utility commands
fstype - Look up a filesystem type
go - start application at address 'addr'
gpio - query and control gpio pins
gpt - GUID Partition Table
help - print command description/usage
i2c - I2C sub-system
iminfo - print header information for application image
imxtract- extract a part of a multi-image
itest - return true/false on integer compare
load - load binary file from a filesystem
loadb - load binary file over serial line (kermit mode)
loads - load S-Record file over serial line
loadx - load binary file over serial line (xmodem mode)
loady - load binary file over serial line (ymodem mode)
loop - infinite loop on address range
ls - list files in a directory (default /)
md - memory display
mdio - MDIO utility commands
mii - MII utility commands
mm - memory modify (auto-incrementing address)
mmc - MMC sub system
mmcinfo - display MMC info
mw - memory write (fill)
nfs - boot image via network using NFS protocol
nm - memory modify (constant address)
part - disk partition related commands
ping - send ICMP ECHO_REQUEST to network host
printenv- print environment variables
pxe - commands to get and boot from pxe files
reset - Perform RESET of the CPU
run - run commands in an environment variable
save - save file to a filesystem
saveenv - save environment variables to persistent storage
setenv - set environment variables
sf - SPI flash sub-system
showvar - print local hushshell variables
size - determine a file's size
sleep - delay execution for some time
source - run script from memory
spl - SPL configuration
sspi - SPI utility command
sysboot - command to get and boot from syslinux files
test - minimal test like /bin/sh
tftpboot- boot image via network using TFTP protocol
true - do nothing, successfully
usb - USB sub-system
usbboot - boot from USB device
version - print monitor, compiler and linker version